## Slide 1
Ver. 01
Course 0
Smart Lamp Project
Copyright @ 2018 Innovaker
Project Overview
Unrestricted

## Slide 2
Raspberry Pi VNC Connection
Connect Raspberry Pi to monitor, keyboard and mouse
Power Pi on and enter into desktop on the Pi
Setup WiFi as picture
Get IP address of Pi by hover curse on the WiFi icon, e.g. 192.168.0.15

## Slide 3
Raspberry Pi VNC Connection
Connect your laptop to WiFi in the same local network as Pi
Install RealVNC viewer on your laptop from this link
  https://www.realvnc.com/en/connect/download/viewer/
Start VNC viewer from your laptop and type in the IP address of the Pi

## Slide 4
Raspberry Pi VNC Connection
4) Following window display, default user name: “pi”, password: “raspberry”, turn on “Remember password” option, the Pi desktop window will be displayed.

## Slide 5
Raspberry Pi VNC Connection
Start Pi with monitor to connect wifi once
Install VNC viewer on laptop
Connect LCD as picture
Restart Pi with LCD connected
VNC to Pi by LCD displayed IP address
Note:
Use micro SD card we provided with proper setting and startup python codes to display IP

## Slide 6
6
Copyright @ 2018 Innovaker
Raspberry Pi 3 GPIO

## Slide 7
Ver. 01
with
Raspberry Pi Programming
Copyright @ 2018 Innovaker
Sensors and Electronic Circuit
Unrestricted

## Slide 8
8
Copyright @ 2018 Innovaker
Buttons and Buzzers
Sample code see ****.py

## Slide 9
9
Copyright @ 2018 Innovaker
Buzzers
A buzzer or beeper is an audio signalling device,[1] which may be mechanical, electromechanical, or piezoelectric (piezo for short). Typical uses of buzzers and beepers include alarm devices, timers, and confirmation of user input such as a mouse click or keystroke.
How does it work?
The buzzer consists of an outside case with two pins to attach it to power and ground.
Inside is a piezo element, which consists of a central ceramic disc surrounded by a metal (often bronze) vibration disc.
When current is applied to the buzzer it causes the ceramic disk to contract or expand. Changing the This then causes the surrounding disc to vibrate. That’s the sound that you hear. By changing the frequency of the buzzer, the speed of the vibrations changes, which changes the pitch of the resulting sound.

## Slide 10
10
Copyright @ 2018 Innovaker
Push Button Switch
Buttons can convert physical changes into electrical signals
How does it work?
If you hold the button such that it is in a vertical orientation, then the two rails that are parallel to each other are connected internally. When the button is pressed down, the switch inside closes, connecting the two rails. Current from one branch can then flow across to the other.

## Slide 11
11
Copyright @ 2018 Innovaker
Connect a Button into Circuit
Pull-up Resistor
Pull-down Resistor
GPIO
GPIO
10k
10k
10k
10k

## Slide 12
12
Copyright @ 2018 Innovaker
Connect a Button with Raspberry Pi
Pull-up Resistor Connection:
Terminal A – 5V power source
Terminal B – GPIO pin (GPIO 25 /Pin 22)
Terminal C – ground
Button Mode:
Un-pushed - GPIO pin detects the 5V signal as an input, and Raspberry Pi will read high as input to the GPIO.
Pushed - all 4 terminals become connected, causing the GPIO pin linked with the ground, and the Pi will read low as input to the GPIO.

## Slide 13
13
Copyright @ 2018 Innovaker
Buttons & Buzzers - Circuit and Code
Button connects to GPIO 25
Buzzer connects to GPIO 19
Python Code:
BUTTON_PIN = 25 # assign GPIO pin 25 to the button BUZZER_PIN = 19 # assign GPIO pin 19 to the buzzer
GPIO.setmode( GPIO.BCM ) # set GPIO pin # mode GPIO.setup( BUTTON_PIN, GPIO.IN, pull_up_down=GPIO.PUD_UP ) GPIO.setup( BUZZER_PIN, GPIO.OUT )

## Slide 14
14
Copyright @ 2018 Innovaker
Methods for Read a GPIO Input
Two ways for read a GPIO input from a button:
Method 1 – Inquiry: continuously read the GPIO input using a loop
Method 2 – Interrupt: only reacts when GPIO input changes

## Slide 15
15
Copyright @ 2018 Innovaker
import RPi.GPIO as GPIO import time | 
BUTTON_PIN = 11 BUZZER_PIN = 4 ON = True OFF = False | Assign pin 11 as button pin Assign pin 4 as buzzer pin
def setup(): GPIO.setmode(GPIO.BCM) GPIO.setup(BUTTON_PIN, GPIO.IN, pull_up_down=GPIO.PUD_UP) GPIO.setup(BUZZER_PIN, GPIO.OUT) | Notice how the button setup differs slightly from that of the other pins. GPIO.setup(BUTTON_PIN, GPIO.IN, pull_up_down=GPIO.PUD_UP) - the button setup takes a third parameter, a function, to determine which state the button is naturally in.
Button & Buzzer - Python Code
Inquiry
Refer file ****.py

## Slide 16
16
Copyright @ 2018 Innovaker
Button / Buzzer - Python Code 2/2
def main(): while True: time.sleep(0.01) if(GPIO.input(BUTTON_PIN) == 0): print ("Button is pressed!") print ("Buzzer will be turn on!") GPIO.output(BUZZER_PIN, ON) else: GPIO.output(BUZZER_PIN, OFF) | GPIO.input(BUTTON_PIN) - Reads the status of the GPIO pin. When the pull_up_down status is GPIO.PUD_UP, the natural state is a 1 while a push is a 0
if __name__ == '__main__': try: setup() main() finally: GPIO.cleanup() | 

## Slide 17
17
Copyright @ 2018 Innovaker
Motion Sensors
Sample code see ****.py

## Slide 18
18
Copyright @ 2018 Innovaker
What is a Motion Sensor
A type of electronic sensor that detects for motion or movement
Used for security systems or motion sensing lights
Two types of motion sensors: active and passive
Active motion sensors: emit ultrasonic waves which are reflected back to the sensor.
Passive infrared sensors: detect infrared or heat signals emitted by humans or other animals.
The sensors included in this project is a passive infrared sensor

## Slide 19
19
Copyright @ 2018 Innovaker
How Does It Work?
The passive infrared sensor has 3 pins:
power (VCC)
ground (GND)
the signal (OUT)
The infrared sensor will detect for any abrupt changes in its infrared signal, and upon detection, will send a digital output to trigger another event.

## Slide 20
20
Copyright @ 2018 Innovaker
Motion Sensor - Electronic Circuit
Motion sensor connects to GPIO 19 (pin 35)
LED connects to GPIO 26 (pin 37)
Python Code:
LED_PIN = 37 MOTION_PIN = 35
GPIO.setmode(GPIO.BCM) GPIO.setup(MOTION_PIN, GPIO.IN, pull_up_down=GPIO.PUD_UP) GPIO.setup(BUZZER_PIN, GPIO.OUT)

## Slide 21
21
Copyright @ 2018 Innovaker
Motion Sensor - Python Code 1/2
motion1.py

## Slide 22
22
Copyright @ 2018 Innovaker
Motion Sensor - Python Code 2/2
motion2.py